Linux, I2C, and me
Michael Welling (m_w)
mwelling@ieee.org
March 8th, 2018

---
whoami
Michael Welling
Embedded Systems Architect
MS in Electrical and Computer Engineering
PCB Design
Linux Board Support
Community Efforts
Beagleboard.org GSoC Mentor
96Boards.org Community Mezzanine Initiative
E-ale.org Instructor
KiCAD Training

---
Overview
- What is I2C?
- Example I2C Devices
- I2C Protocol
- Linux I2C Subsystem
- Linux I2C Drivers
  - I2C Bus Drivers
  - I2C Device Drivers
  - I2C Slave Interface
- Instantiating I2C Devices
- User-space tools
- Demo
- Questions

---
What is I2C?
- I2C stands for inter-integrated circuit
- First developed by Philips Semiconductor in 1982
- Synchronous multi-master multi-slave serial bus
- Half duplex protocol
- Open-drain signaling
- Only two signal wires
  - SDA: data
  - SCL: clock
en:user:Cburnett, I2C, CC BY-SA 3.0
https://en.wikipedia.org/wiki/I%C2%B2C

---
What is I2C?
- I2C addressing is typically 7 bits per the original specification
- I2C clock speed is typically 100KHz per the original specification
- Later versions of the specification introduced faster clock modes and 10 bit addressing:
  - Version 1 added 400KHz Fast mode and 10 bit addressing
  - Version 2 added 3.4MHz Hs mode
  - Version 3 added 1MHz Fast mode+ and ID mechanism
  - Version 4 added unidirectional 5Mhz Ultra Fast mode
- SMBus (System Management Bus) is a subset of I2C defined by Intel
  - Typically used on PC motherboards for power control and sensors
  - Stricter tolerances on voltage levels and timing
  - Adds an optional software level address resolution protocol

---
Example I2C Devices
- Real time clock
- EEPROM
- Analog converters (ADC, DAC)
- Sensors (Temperature, Pressure)
- Microcontrollers
- Touchscreen controllers
- GPIO expanders
- Monitor and TV adapters

---
Example I2C Hardware

---
I2C Protocol
Start
SDA goes low before SCL to signal the start of transmission.
Addr
7 bit address that determines the slave device to be accessed.
R/W
Transaction data direction bit. (1 = read, 0 = write)
Data
Byte data read from or written to the slave device. Can be multiple bytes.
ACK
Acknowledge bit. (0 = ack, 1 = nak)
Stop
SDA goes high after SCL to signal the end of transmission.

---
Linux I2C Subsystem
- Early implementations were from Gerd Knorr and Simon G. Vogl.
- Migrated to the device model by Greg KH in late 2.5 versions of Linux.
- Integrated into standard device driver model by David Brownell and Jean Delvare in Linux 2.6.
- Currently maintained by Wolfram Sang.

---
Linux I2C Subsystem
https://i2c.wiki.kernel.org

---
Linux I2C Subsystem
List: linux-i2c;     ( subscribe / unsubscribe )
Info:
Linux kernel I2C bus layer mailing list.
Archives:
http://marc.info/?l=linux-i2c
http://www.spinics.net/lists/linux-i2c/
https://git.kernel.org/pub/scm/linux/kernel/git/wsa/linux.git/

---
Linux I2C Drivers
I2C Bus Drivers
  Bus	→	Algorithm
        Adapter
An Algorithm driver contains general code that can be used for a whole class of I2C adapters. Each specific adapter driver either depends on one algorithm driver, or includes its own implementation.
https://www.kernel.org/doc/Documentation/i2c/summary

---
Linux I2C Drivers
I2C Device Drivers
  Device	→	Driver
        Client
A Driver driver (yes, this sounds ridiculous, sorry) contains the general code to access some type of device. Each detected device gets its own data in the Client structure. Usually, Driver and Client are more closely integrated than Algorithm and Adapter.
https://www.kernel.org/doc/Documentation/i2c/summary

---
Linux I2C Drivers
I2C Slave Interface
        e.g. sysfs I2C slave events I/O registers
  +-----------+ v +---------+ v +--------+ v +------------+
  | Userspace +........+ Backend +-----------+ Driver +-----+ Controller |
  +-----------+ +---------+ +--------+ +------------+
        | |
  ----------------------------------------------------------------+-- I2C
  --------------------------------------------------------------+---- Bus
echo slave-24c02 0x1064 > /sys/bus/i2c/devices/i2c-1/new_device
https://www.kernel.org/doc/Documentation/i2c/slave-interface
https://www.youtube.com/watch?v=JdQ21jlwb58

---
Instantiating I2C Devices
Device tree
        i2c1: i2c@400a0000 {
        /* ... master properties skipped ... */
        clock-frequency = <100000>;
        flash@50 {
        compatible = "atmel,24c256";
        reg = <0x50>;
        };
        pca9532: gpio@60 {
        compatible = "nxp,pca9532";
        gpio-controller;
        #gpio-cells = <2>;
        reg = <0x60>;
        };
        };

---
Instantiating I2C Devices
Platform device
static struct i2c_board_info h4_i2c_board_info[] __initdata = {
        {
        I2C_BOARD_INFO("isp1301_omap", 0x2d),
        .irq = OMAP_GPIO_IRQ(125),
        },
        { /* EEPROM on mainboard */
        I2C_BOARD_INFO("24c01", 0x52),
        .platform_data = &m24c01,
        },
        { /* EEPROM on cpu card */
        I2C_BOARD_INFO("24c01", 0x57),
        .platform_data = &m24c01,
        },
};
static void __init omap_h4_init(void)
{
        (...)
        i2c_register_board_info(1, h4_i2c_board_info,
        ARRAY_SIZE(h4_i2c_board_info));
        (...)
}

---
Instantiating I2C Devices
From user-space
echo eeprom 0x50 > /sys/bus/i2c/devices/i2c-3/new_device
https://www.kernel.org/doc/Documentation/i2c/instantiating-devices

---
User-space Tools
- Simple character device driver (i2c-dev)
  - Device nodes at /dev/i2c-x
  - Slave address set by I2C_SLAVE ioctl.
  - Simple access using read() / write()
  - i2c_smbus_{read,write}_{byte,word}_data()
- i2ctools
  - i2cdetect
  - i2cget
  - I2cset
https://www.kernel.org/doc/Documentation/i2c/dev-interface

---
Demo
Hold my beer and watch this.
[Speaker Notes: Debian I2C tools demo i2cset 2 0x1c 0x2a 0x00 i2cset 2 0x1c 0x0e 0x00 i2cset 2 0x1c 0x2a 0x01 while [ 1 ]; do yes | i2cdump -r 1-6 2 0x1c; done]

---
Questions?
My name is Michael Welling, ask me anything.